## Slide 1
Digital Design using VHDL

## Slide 2: Digital Design using VHDL
Binary Counter and variants
Group 2 :
Ngô Văn Cảnh - 20193204
Nguyễn Danh Khuê - 20193224
Phùng Mạnh Dũng - 20193210

## Slide 3
Binary Counter and variants
Free-running Binary counter
Universal Binary counter
Mod-M Binary counter
But first of all…

## Slide 4
But first of all…

## Slide 5
What is a Binary Counter ?
But first of all…
A binary counter circulates through a binary sequence repeatedly.

## Slide 6
What is a Binary Counter ?
A binary counter circulates through a binary sequence repeatedly.
For example, a 4-bit binary counter counts from “0000", "0001 “ , . . . , to " 1111" and wraps around.
But first of all…

## Slide 7
What is a Binary Counter ?
A binary counter circulates through a binary sequence repeatedly.
The simplest form of counter is called Free-running Binary Counter. Besides of the n-bit output, it takes clock and reset as input and a Max_tick output which active whenever output is full ( output = 2n -1 )
For example, a 4-bit binary counter counts from “0000", "0001 “ , . . . , to " 1111" and wraps around.
4-bit Binary Counter
4-bit Binary Counter
clk
rst
Max_tick
Output

## Slide 8
What is a Binary Counter ?
A binary counter circulates through a binary sequence repeatedly.
4-bit Binary Counter
clk
rst
Max_tick
Output
For example, a 4-bit binary counter counts from “0000", "0001 “ , . . . , to " 1111" and wraps around.
The simplest form of counter is called Free-running Binary Counter. Besides of the n-bit output, it takes clock and reset as input and a Max_tick output which active whenever output is full ( output = 2n -1 )

## Slide 9
Free-running Binary Counter
module free_run_bin_counter #(parameter N=8)
(
output reg [N-1:0] q,
output max_tick,
input clk, rst
); always @(posedge clk, posedge rst)
if(rst)
q <= 0;
else
q <= q + 1;
assign max_tick = (q == 2**N - 1) ? 1 : 0;
endmodule

## Slide 10
Free-running Binary Counter
module free_run_bin_counter_tb;
reg clk,rst;
wire max_tick;
wire [3:0] q; free_run_bin_counter#(4) test(q, max_tick, clk, rst); //4 bit counter initial begin
clk = 0;
forever #10 clk = ~clk;
end
initial begin
rst = 1;
#34 rst = 0;
#200 rst = 1;
#50 rst = 0;
#1000 $stop;
end initial begin
$monitor($time," rst = %b , q = %b , max_tick = %b",rst,q,max_tick);
end
endmodule